502 - A/G – Visual Bombing Modes

Radar Ranging Notes
- Radar Ranging activates in DYK, ARAK AKAN, and RB-75 modes, before trigger unsafe. In PLAN mode, ranging starts at trigger unsafe.
- Ranging is indicated by the "fin" and ranges to the spot under the reticule dot.
- Bank angle must be under 45°.
- When Radar Ranging is in use the CI is blank.
- When the sight angle is less than 5° from the horizon, the sight instead shows a fixed range of 1400m. The computer does not provide firing or pullup commands in this mode.
- Disable Radar Ranging with TAKT 253
Bombing Tips
Release interval of 10-30m will produce a coherent stick of bombs, above 30m will lead to some un-asploded gaps between the bombs.

M/71 bombs -- 120 kg (265 lb) GP bombs, 4 per pylon

DYK mode

Dive Bomb
(recommended to use a pop-up point)

1. Weapon Selector dial ... DYK
2. Interval dial ... as needed (distance in m)
3. Release Mode switch ... SERIE (default)
4. Master Mode dial ... ANF (precision, uses radar ranging)
5. Set QFE on altimeter to value shown in kneeboard for target waypoint. (optional )
6. Place pipper on target, and then hold trigger UNSAFE to designate it.
7. Hold WEAPON RELEASE AFTER the time/distance line flashes, but BEFORE the wings cue appears.
8. Follow the steering cue circle while continuing to hold trigger.
9. Bombs will fall automatically.

Dive Bomb (low precision)

Same procedure as above, but QFE is mandatory, stay in NAV mode, UNSAFE to show symbology, the bombs will drop immediately upon pulling the trigger to roughly where the pipper shows.
1. Weapon Selector dial ... DYK
2. Interval dial ... as needed (distance in m)
3. Release Mode switch ... SERIE (default)
4. Master Mode dial ... NAV
5. Set QFE on altimeter to value shown in kneeboard for target waypoint. (Required!)
6. Trigger UNSAFE to show symbology. You're now in a barometric-altitude-informed CCIP mode, the bombs will land where you put the pipper.
7. When the "wings" cue appears, PULL AND HOLD Weapon Release.
8. Bombs will drop immediately.

PLAN mode

Level CCRP Bomb

1. Weapon Selector to PLAN.
2. Sight mode selector to desired release interval.
3. Master mode ANF.
4. Place the pipper on the intended target. When the pipper is on the target, TRIGGER UNSAFE to designate. Radar ranging will begin.
5. When the "wings" appear, pull and HOLD WEAPON RELEASE.
6. Follow the Steering Cue Ring
7. Bombs will release automatically.
8. After FÄLLD LAST, SAFE the trigger, master mode NAV, turn and egress.

Direct Bomb
This mode exists for when you are bombing in formation. The flight leader is assumed to be using some release release mode, and delivers an instruction over the radio for when to release.

1. Weapon selector to PLAN.
2. Sight selector to desired release interval.
3. Master mode NAV.
4. Release the trigger on command, bombs will fall immediately.