307 - Flight – Time On Target

Notes
- TID, OUT displays time to the next point in your flight plan (including takeoff) to hit your time-on-target. If the leading digit is blank, you are behind schedule and the numbers are counting down to the next waypoint. If the leading digit is 9, you are ahead of schedule and should slow down.
- If flying with a flight, make sure you have the same time and speeds. It is smart to click your release waypoint and verify that you are all scheduled to release at the same time.
- RB-15 flight time at max range is about 4 minutes, use this to sanity check your release point time vs ToT.
- Ingress Mach lasts until the next Ingress point, or if there is none, after a target point. If you want to get away from a target at a defined speed, make sure you have another defined ingress point afterwards!
- Default is 0.55

Setting Time On Target For Markpoint Attack
During mission planning, before takeoff.
If flying with RB-15 or other weapon that uses markpoints, set the markpoint on target and use your intended release point as an M point.
To set attack parameters: (RB-15 only)
1. Computer selector to TID, IN
2. Input the time you want your missiles to hit (use time from F10 map), HHMMSS
3. Click Bx, then 8 to specify markpoint 8. (if using an M target waypoint, hit that number instead)
4. TID OUT now shows your time to takeoff.
To set route parameters:
Note, you cannot set mach to waypoint 1, so you should set it close to the starting field.
1. Computer TID, IN
2. Enter target mach from the waypoint you intend to modify.
3. Choose the waypoint to set that speed from (B1...B8)
4. TID OUT now shows your time to takeoff, which is probably longer than what it was before because the default speed is 0.5 mach.
5. If the TID OUT time is really slow you may wish to change the target time.

If you accidentally hit LS after entering TID, you changed the clock on the viggen. Fix it the same way you broke it.

Economic Speeds