502 - A/G - BK 90 glide cluster bombs

Mixed weapon loadouts
Mixed loadouts are not valid, except the following: RB-24/-24J A2A missiles are allowed with any loadout, and AKAN 30 mm gunpods are allowed with RB-75 (Maverick) or RB-05A (MCLOS) missiles.

Using Radar To Find Targets:
1. Make sure you have a good nav fix using TERNAV or enroute waypoint fixes.
  1. Remember that doing radar fixes on M target points don't correct your ownship position, which is crucial for weapons like BK-90
2. Higher altitude = better picture but more danger. 400 is okay for lightly defended targets.
3. Ground targets may start to be made out at around 30km.
4. Play with antenna elevation and gain to try to get better contrast on a ground contact.
5. Use Bx1-5 (markpoints) to identify targets of opportunity. Make sure that you have estimated the QFE well, the dispenser has a barometric altimeter that inherits QFE from the CK-37

BK 90 Mjolnir glide cluster bomb -- MJ1 is 72x HE/frag bomblets, MJ2 is 24x AP bomblets
1. Weapon Selector dial ... ATTACK
2. Release Mode switch ... SERIE (default)
3. Set QFE on altimeter to value shown in kneeboard for target waypoint.
4. Default bomb approach altitude is 60 m AGL (internal radar altimeter). Note this altitude is approach, (to clear obstacles and avoid air defense enroute) not release, release altitude is not alterable. To change:
  1. Set Targeting Mode switch to VALB (default). (If set to STD, height will be 60 m.)
  2. Set TAKT - IN.
  3. Enter 91, then three digit altitude in m (30 to 500 m).
     910300 = 30 m, 915000 = 500 m. Default is 60 m (or 910000).
  4. Press LS, then set AKT POS - OUT.
5. Default bomb pattern is Compact, both bombs burst over same location. Bomb patterns only work if dropping both bombs in SERIE. To change:
  1. Set TAKT - IN, then enter:
    - 921000 for Long (bombs burst in line one after the other)
    - 922000 for Wide (bombs burst next to each other)
    - 923000 or 920000 for Compact (default)
  1. Press LS, then set AKT POS - OUT.
2. When approaching target waypoint, set Master Mode dial to ANF.
3. Speed 0.6 to 0.9 Mach. Use Stage 2 AB for about 0.85 Mach.
4. Height 50 m to 500 m.
5. Hold trigger UNSAFE to show HUD symbology.
6. Starting about 10 km away, distance bars will appear at bottom of HUD. When horizontal line is within the outer vertical bars, target is in range. Max range is about 6 to 7 km at 0.9 Mach
7. Hold down trigger to release. First bomb will release about 1.3 seconds after trigger is held, second one will be 1.5 sec later. You must press the trigger again to drop the second pair if you're carrying 4.