306 - Flight - Countermeasures, ECM, ELINT

Chaff and Flares dispenser -- KB F/C dispenser (stations 2 and 6)
- CMS Hat forward is Quick Release Button (toggle, button on IRL throttle). This begins firing 1 chaff and 1 flare, every 2 seconds, giving 3m30s of chaff and 1m12s of flares.
  - Use KB type knob to select Chaff only (R), Flares only (F), or both Chaff and Flares (RF).
- CMS Hat Back/Left/Press is Countermeasures Dispense Switch (switch on left forward canopy rail). Back dispenses continuously, Left dispenses in an interval, Press to cancel. This dispenses Chaff only, no Flares. See table below for settings.
- Pods have 72 flares and 212 chaff each. Changing these quantities breaks the dispense interval settings (openbeta 2.7.11.21408.1 patch notes).
- Flares can only be released with Quick Release button, with KB type knob set to RF or F. Previous program will resume after Quick Release, except Slow Streak (reset by cycling KB streak selector knob to 0 and back to 4).
- On warning light panel:
  - KB-V SLUT = Left countermeasures pod empty
  - KB-H/KA SL = Right countermeasures pod empty (or ECM pod warming up or fail)
  - FACKL SL = Flares empty
Countermeasures modes and settings:
Mode name	KB mode knob	KB streak knob	KB type knob	KB dispense switch (CM Hat L/B)	Interval and total
Rapid	1	0	R or RF	INT or KONT	0.85 sec, 1.5 min
Medium	2	0	R or RF	INT or KONT	2.0 sec, 3.5 min
Slow/Slow streak	3	0 for both pods in parallel, 4 for series	R or RF	FRAN	4.5 sec, 8 or 16 min (parallel or series)
Automatic APP-27 (internal RWR)	A	0	R or RF	INT or KONT	2.0 sec, when RWR detects lock
Automatic U22	A	0	R or RF	KONT	0.85 sec, when U22 detects lock
Quick release button (CM Hat forward/back)	any	any	R, RF, F	--	2 sec, 3.5 min chaff, 1.2 min flares

ECM jammer and ELINT -- U22 and U22/A pods (station 6 only)
- U22 pod is mid-1980s ECM only
- U22/A pod is mid-1990s ECM + ELINT
Pod	Mode	Mode selector knob	Bandwidth selector knob
U22	Off	0	any
	Automatic	A	any
	Standby/Warmup (3 mins)	B	any
	Always on jamming	E	any
U22/A	Off	0	any
	Standby/Warmup (3 mins)	A	F
	Silent recording	A	G: low sensitivity / H, J: high sensitivity / K: automatic cycling between G and J
	Reactive jamming	B, D, E	F, G, H, J, K

- On warning light panel:
  - KB-H/KA SL = ECM pod warming up or fail (or right countermeasures pod empty). If fail, pressing Master Caution reset will restart the pod.
  - MOTVERK = ECM pod is emitting or ELINT is active
- Jammer emits only to the front (+/-60 deg horizontal, +/-45 deg vertical). (Not sure if this is modeled in DCS.)
- Very effective for sams, can get within 20km, nearly maverick range.
ELINT with U22/A pod
1. Jamming Mode knob ... A
2. Jamming Bandwidth knob ... K
3. Pod will record emitters and their bearing over time. MOTVERK will flash at different rates as it records
4. After landing, set Master Mode knob to BER to reset nav computer and compile and write the ELINT data. Built-in kneeboard page will also show emitters recorded and locations.
5. Data is written to C:\Users\<username>\Saved Games\DCS_AJS37\ELINTData.info.
6. Load the data into https://elint-app.firebaseapp.com/ to map it.