402 - A/A - Gun, IR, SARH missiles

Fence In
Master Arm ... ON (B2 button to toggle)

30 mm cannon -- 2x DEFA 553, 150 rounds per gun
1. Press Trigger to fire. Trigger always fires guns as long as Master Arm is ON.
2. (Optional)Press Dish Hat Down C+SW/M button to enter dogfight mode.
3. (Optional) Press Manvr/PC Hat Up to automatically lock the target.
4. If you do not have a radar lock, you will have a gyroscopic sight. This can be adjusted for 300m or 600m range. The gyroscopic sight needs to remain on a target for 2 sec befor the solution is “valid”. Fly so that the target’s wingspan touches the diamonds.
5. If you have a radar lock, placing the pipper on the target should be a good firing solution instantly.
- If the Automatic/Manual firing switch is FWD, the gun will fire when the pipper is on target without pilot input.
- If the Single/Salvo selector switch is in CPC, gun firing is controlled by the burst limiter, which is configured on the ground in mission editor weapons settings.

Available radar ACM modes (automatic lock, 7km range):
- PC/VR Hat Up: TL mode automatically locks target roughly in the HUD glass
- PC/VR Hat Dn: BZ mode Works similarly but with a larger scan area that is slewable (not implemented)
Matra R.530
- When both missiles are selected, firing priority is as follows:
  - Locked missile has priority.
  - If both are locked, IR missile has priority.
  - If both are same seeker type, left missile has priority.
- R.530 IR missile has 20 minutes of coolant, and takes 20 seconds to cool the seeker head. Cooling begins when Master Arm is on and missile is selected on armament panel??

R.550 Magic, AIM-9, and R530F IR missiles
1. Ensure Fuel Dipper FWD, Sight selector MID, Missile Preparation Switch FWD, Single/Salvo FWD (CPC)
2. Press Dish Hat Down to select Magic missiles.
  1. If you want to choose a particular missile, press the EXT D or EXT G station select buttons. Default is Left (G)
  2. Selecting MGFUS or MD is is required for R530F Missiles.
3. Missile cooling takes up to 20 seconds, and then the missile stays cool for 20 minutes.
4. When missiles are ready, triangles appear on the HUD.
5. The missile is boresighted to the top of the HUD glass. When you hear the tone, hold Red Button to fire. (the engine RPM will dip to reduce ingested smoke)
R.530F EM Missile (with auto radar lock)
1. Set Radar Mode Switch FWD, Fuel dipper FWD, Sight selecter MID, Missile Prep Switch FWD, Single/Salvo FWD, Normal/Jammer Pursuit Switch LEFT, R350 Altitude Difference AFT (unless attacking a high and fast target), Fore/Aft selector switch AFT (fwd is for use in a jamming envonment where target range is not available), Automatic/Manual Firing AFT (manual).
2. The R530 can be used with any a2a radar mode, including HA, IC, TL, or BZ. Use any of these to lock a target.
3. Your radar screen will now indicate the target range and velocity of closure. A square on the HUD will tell you the position, and “wings” steering cues will tell you how to fly to intercept.
4. When a missle is tracking, an orange circle will appear below the triangle.
5. When you are within good range, a green circle will appear.
6. Once you have locked a target, VERIFY THAT IT IS HOSTILE, either visually or with AWACS. If you are certain the target is hostile, press red button.
  1. If you are outside of the missile launch parameters, a red “abort” circle will appear on the HUD. These may include:
    - Roll angle greater than 80 deg.
    - Acceleration below -1 or above 4g
    - Negative pitch angle when flying below 8000 ft
    - Target within 500m
Keep the target in sight, the missile requires continuous guidance until impact.