501 - A/G - Bombs, Rockets, Guns

Mixed weapon loadouts
Mixed loadouts are not valid, except the following: RB-24/-24J A2A missiles are allowed with any loadout, and AKAN 30 mm gunpods are allowed with RB-75 (Maverick) or RB-05A (MCLOS) missiles.

M/71 bombs (high drag) -- 120 kg (265 lb) GP bombs, 4 per pylon
1. Weapon Selector dial ... SJO PLAN (default)
2. Interval dial ... as needed (distance in m)
3. Release Mode switch ... SERIE (default)
4. Master Mode dial ... NAV
5. Set QFE on altimeter to value shown in kneeboard for target waypoint.
6. Hold trigger UNSAFE (Trigger 1st stage) to show HUD symbology.
7. Bombs will fall between dot and circle.
8. Speed 0.7 to 0.9 Mach. Use Stage 2 AB for about 0.85 Mach.
9. Release height 50 m to 200 m.
10. Hold Trigger 2nd stage to drop until all bombs are gone.

ARAK M/70B rockets -- 135 mm (5.3 in), 6 per pod, HE-Frag or HEAT
Short range mode (1 km to 3 km)
1. Weapon Selector dial ... ATTACK
2. Release Mode switch: NORM/SERIE (up, default) for Short Range
3. Second Release Mode switch switch:
  1. GRUPP/VALB (up) for all rockets per pod (press trigger once fires all rockets in 0.6 sec).
  2. ENKEL/STD (down) for single rocket per pod per trigger press
4. When approaching target waypoint, Master Mode dial:
  1. ANF for automatic continuous target ranging
  2. NAV for manual target ranging (hold Trigger Unsafe to range)
5. (optional) Set QFE on altimeter to value shown in kneeboard for target waypoint. (Not required, only affects the placement of the target indicator ring, not the rocket accuracy.)
6. Pop up and dive on the target. Must be diving more than 5 deg for radar ranging to work.
7. Put small solid center dot on the target. Hollow ring should show location of target.
8. Hold Trigger Unsafe to begin radar ranging (if in NAV mode). Target indicator ring will disappear.
9. Distance line at bottom flashes when within 2 seconds of release.
10. When in range, "wings" appear to either side of center dot. Press and hold trigger to fire.
Long range mode (6 km to 7 km)
1. Weapon Selector dial ... ATTACK
2. Release Mode switch: LA/IMP (down) for Long Range
3. Second Release Mode switch switch:
  1. GRUPP/VALB (up) for all rockets per pod (press trigger once fires all rockets in 0.6 sec). Recommended for long range mode.
  2. ENKEL/STD (down) for single rocket per pod per trigger press
4. When approaching target waypoint, Master Mode dial:
  1. ANF for automatic continuous target ranging
  2. (Cannot be in NAV mode for long range rockets)
5. (optional) Set QFE on altimeter to value shown in kneeboard for target waypoint. (Not required, only affects the placement of the target indicator ring, not the rocket accuracy.)
6. Pop up and dive on the target. Must be diving more than 3 deg for radar ranging to work.
7. Put small solid center dot on the target. Hollow ring should show location of target.
8. Hold Trigger Unsafe. Target indicator ring will disappear??
9. Distance line at bottom flashes when within 2 seconds of release.
10. When in range, "wings" appear to either side of center dot. Press and hold trigger to fire.

AKAN 30/55 gun pods -- 30 mm, 150 rounds per pod
1. Weapon Selector dial ... ATTACK
2. Release Mode switch ... SERIE (default)
3. When approaching target waypoint, Master Mode dial ... ANF
4. Set QFE on altimeter to value shown in kneeboard for target waypoint. (Not strictly required?? Seems to only affect the placement of the target indicator ring, not the rocket accuracy.)
5. Pop up and dive on the target. Must be diving more than 5 deg for radar ranging to work.
6. Put center dot on the target. Target indicator ring should show location of target.
7. Hold Trigger Unsafe to begin radar ranging. Target indicator ring will disappear.
8. Distance line at bottom flashes when within 2 seconds of release.
9. When in range, "wings" appear to either side of center dot. Press and hold trigger to fire.