501 - A/G – Low-drag Bombs

Mixed weapon loadouts
Mixed loadouts are not valid, except the following: RB-24/-24J A2A missiles are allowed with any loadout, and AKAN 30 mm gunpods are allowed with RB-75 (Maverick) or RB-05A (MCLOS) missiles.

M/71 bombs (low drag) -- 120 kg (265 lb) GP bombs, 4 per pylon

Dive Bomb
(recommended to use a pop-up point)

1. Weapon Selector dial ... DYK
2. Interval dial ... as needed (distance in m)
3. Release Mode switch ... SERIE (default)
4. Master Mode dial ... ANF (precision, uses radar ranging)
5. Set QFE on altimeter to value shown in kneeboard for target waypoint. (optional )
6. Place pipper on target, and then hold trigger UNSAFE to designate it.
7. Hold Trigger 2nd Stage AFTER the time/distance line flashes, but BEFORE the wings cue appears.
8. Follow the steering cue circle while continuing to hold trigger.
9. Bombs will fall automatically.

Dive Bomb (low precision)

Same procedure as above, but QFE is mandatory, stay in NAV mode, half-pull to show symbology, the bombs will drop immediately upon pulling the trigger to roughly where the pipper shows.

Radar Bomb

(wip)

Plan Bomb

(wip)

NAV bomb

(wip)

TOSS bomb

(wip)