601 - Notes, Quirks, and Trivia

- For naval attacks, the radar performs best at 300-350m. For ground attack you may wish to go higher, 400ish
- TERNAV System will automatically provide nav fixes based on terrain profile as long as you fly below 500m on your pre-planned course line, and are flying over recognizable terrain features. When the computer is in nav mode, the second from the rightmost digit shows the terrain elevation recognition system status. 2 means the system is active, 3 means it is scanning, 5 means it knows where you are and is making corrections to the dead reckoning system.
- The final digit is the estimated drift.
- TAKT setting in Out mode tells you which pylons are occupied.
- To reset the radar elevation, slam the knob all the way down so that you see a really fast sweep. Then lift it up gradually until the sweep reaches full width of the screen, and then no further. That's the default elevation.
- Default radar elevation is looking down a bit. To search targets far away, especially on open sea, you need to raise the antenna a bit.
- To get takeoff symbology again after landing, click RENSA on the CK-37 data panel, then reload cart.