307 - Flight – Time On Target

Notes
- The closer the pop-up, the safer it is, but more difficult. 7-10 km distance with 30 degree offset from the ingress track is a good starting point.
- Heatblur guy on reddit's recommendations:
  - rockets & bombs, 6-8km
  - RB75 or RB05, 10km
- When planning a pop-up attack, it may be wise to bring countermeasures, using the rapid program in case of manpads, and jamming pod in case of radar aaa.
- Pop-up attacks are usually initiated from 500-800 meter peaks.

Setting Pop Up Point
During mission planning, before takeoff.
A popup point (U) is defined by the direstion and distance from the pop-up point to the target waypoint in a 3 digit heading and 2 digit distance.
1. Computer selector to TAKT, IN
2. Input heading you wish to attack along, and the distance to place the pop-up point in whole kilometers.
   Eg, 165100 will set a popup point of heading 165 from the popup point to the target point at a distance of 10km
3. Press the desired waypoint button. Doing so will make the waypoint a target point if it isn't already.
4. TAKT OUT now shows the location of the popup point, and pressing a waypoint button will navigate you to that point instead of the waypoint itself. Press the waypoint button again to skip the popup point and get navigation instructions directly to the waypoint.

Performing the attack

1. Fly to the pull-up point. When reaching it, pull up 10-15 degrees.
2. When you reach 500m AGL (referenced to the target QFE) look for the target (should be near your canopy bow) and turn in. You should be in a ¾ inversion as you pull the target into the hud.
3. Roll wings level, maintaining descent angle. You should be around 500m AGL again as you begin your attack.