1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Ground - Cold Start

Cold Start Checklist -- Auto Start is much slower
1. Battery switch ... ON (B1 right console front)
2. APU switch ... ON (Shift-B1 left console behind throttle)
3. Canopy ... CLOSE (B5)
4. Left, right, and center MFDs, HUD, and HMD ... On (knobs above MFDs and on UFC, HMD on far right side of instrument panel)
5. When APU light is green: Engine crank switch ... RIGHT (B2 or left console behind throttle)
6. When right RPM over 15%: Right throttle ... IDLE (Lift R Throttle) (left console)
7. INS knob ... CV (carrier) or GND (ground), then press STD HDG OSB on HSI page to use Stored Heading for faster alignment (right console)
8. Engine crank switch ... LEFT (Shift-B2left console behind throttle)
9. When left RPM over 15%: Left throttle ... IDLE (Lift L Throttle)
10. RADAR knob ... OPER (right console next to INS knob)
11. OBOGS switch ... ON (left console near back)
12. FCS Reset button ... press and hold for about 5 seconds (B3 left console, behind throttle)
13. Flaps switch ... HALF
14. Takeoff trim ... Press Trim Reset button (B4), or manually +12° elevator nose up.
15. HOOK BYPASS switch ... FIELD or CARRIER as needed (left console vertical panel)
16. ANTI-SKID switch ... ON for shore, OFF for carrier (left console vertical panel)
17. Radar Altimeter ... On, (Brake Hat Down) and set bug as desired (right console vertical panel)
18. Bleed Air outer knob ... Cycle (right-click all the way around back to NORM) (right console)
19. Backup attitude indicator ... Uncage and align (mouse wheel down)
20. Clear BIT master caution error ... Go to BIT page (in SUPT menu on any MFD) and press STOP OSB.
21. When INS is aligned (0.5 OK or 0.6 OK on HSI page): INS knob ... IFA if year is 1986 or later, or NAV if before.
22. Align HMD:
  1. Press MENU OSB 2x to go to SUPT page, then press BIT OSB.
  2. Press DISPLAYS OSB on top right.
  3. Press HMD OSB to begin self-test. When test patterns have repeated and look good, press STOP OSB.
  4. Press MENU OSB 2x to go to SUPT page, then press HMD OSB (left row center).
  5. Press ALIGN OSB. Crosses will appear on HMD and HUD.
  6. Move head to align the crosses, then press and hold Cage/Uncage button (rear thumb button) for 2.5 seconds to go to FA DX/DY (fine alignment).
  7. For fine alignment, use TDC ministick to align the crosses on the HUD, then press Cage/Uncage button (rear thumb button) to go to FA DROLL.
  8. For roll alignment, use TDC ministick left/right to align the cross to the vertical dropline on the HUD. (Press Cage/Uncage button (rear thumb button) again to toggle back to FA DX/DY if needed.) When both crosses are aligned, press ALIGN OSB to unbox it and save the alignment.
23. Ground Crew ... Remove wheel chocks if needed
24. Parking Brake ... Release (t-handle under jettison button) (don't release parking brake until INS is aligned)

Proceed with rest of preflight checklist on next page.