401 - A/A - Gun and Sidewinder

AKAN 30/55 gun pods -- 30 mm, 150 rounds per pod
1. Weapon Selector dial ... AKAN JAKT
2. Master Mode dial ... ANF
3. Radar ... ON in A1 mode (PPI display) (Flaps Lever Middle)
4. Put dot on target and press Radar T1 detent (trigger half-pull) to lock radar and provide ranging.
  - Or set manual wingspan with Weapon Interval dial, sets wingspan in meters. Wingspan markers show visual span at 500 m.
1. Does not calculate lead, only drop based on range??
2. Hold Trigger Unsafe. Fire when the time/distance line reaches the event markers, or wingspan markers envelop the target.
3. Press Trigger 2nd detent to fire.

RB 24, RB 24J, RB 74 Sidewinders
1. Select Sidewinders:
  1. Press Autothrottle disconnect/IR-missile fast select (Dish Hat Down) to select Sidewinders.
    - Subsequent presses cycle through stations. Selected station is shown in data readout with flashing number.
  1. Or set Weapon Selector dial to IR-RB.
2. Trigger Unsafe (Flip-Down Trigger Active).
3. Put target inside missile boresight area on HUD (between the 3 vertical lines).
4. When you have a higher pitched tone, press Uncage button (Red Pinky Button) to uncage the seeker head. Ring indicator should appear on the target.
5. Pull Flip-down Trigger to fire.

Stores info
- RB 24	AIM-9B (rear aspect)
- RB 24J	AIM-9J or AIM-9P3 (rear aspect, but longer range and better seeker)
- RB 74	AIM-9L (all aspect)