101 - Controls - Joystick
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-, L-*=Long-

Trigger
- P1: T1	(release: T0)
- P2: TV
Flip-down trigger
Up: Trigger SAFE	Down: Trigger ARM	Pull: Weapon release
Red button
P: Weapon release	S-P 3x: Eject
Upper Gray Button -- Toggle HUD Glass Up/Down	Shift --
Lower Gray Button -- Reference button (used to set runway heading and autopilot altitude)
Trim Hat (don't use axis mode)
In normal f‌light:
U/D/L/R: Pitch/Roll Trim
When autopilot is active:
- U/D: Set autopilot altitude
- L/R: Perform standard-rate turn left/right
MANVR/PC hat – Autopilot Control & Weapon Select
- U: Altimeter Medium speed up	S-U:
- D: Altimeter Medium speed down	S-B:
- L: Altimeter Fast down	S-L: Attitude Hold
- R: Altimeter Fast up	S-R: Altitude Hold (also sets att)
Dish hat (pov) -- Weapon Select
- U:
- D: Autothrottle disconnect/IR-missile fast select
- L: Weapon Selector Dial Prev
- R: Weapon Selector Dial Next
- P:
Dish Hat (axis) -- RB-05
- U/D/L/R: RB 05 stick up/down/left/right
- S-U: Switch input with flight stick (use main flight stick to steer missile)
Index Finger Hat -- View and Game controls
- F: VR Telescope	S-F: Rearm
- B: VR Zoom	S-B: Active Pause
- U: Mouse Click	S-U: Scroll Down
- D: Mouse Right Click	S-D: Scroll Down
- P: VR Reset	S-P: show controls
Thumb Reset Hat – Countermeasures and Altimeter
- F: Quick Chaff/Flare Dispense	S-F: ECM Band CCW
- B: CMS Dispense KONT/OFF	S-B: ECM Band CW
- L: CMS Dispense INT/Off	S-L: ECM Mode CCW
- R: --	S-R: ECM Mode CCW
- P: CMS Dispense OFF
- S-P: Toggle dampers (SPAK)
Brake lever -- Switch input with flight stick (use main flight stick to steer missile)
Grip Button -- SHIFT