501 - A/G – Low-drag Bombs

Mixed weapon loadouts
Mixed loadouts are not valid, except the following: RB-24/-24J A2A missiles are allowed with any loadout, and AKAN 30 mm gunpods are allowed with RB-75 (Maverick) or RB-05A (MCLOS) missiles.

M/71 bombs (low drag) -- 120 kg (265 lb) GP bombs, 4 per pylon

Dive Bomb
(recommended to use a pop-up point)

1. Weapon Selector dial ... DYK
2. Interval dial ... as needed (distance in m)
3. Release Mode switch ... SERIE (default)
4. Master Mode dial ... ANF (precision, uses radar ranging)
5. Set QFE on altimeter to value shown in kneeboard for target waypoint. (optional )
6. Place pipper on target, and then hold trigger UNSAFE to designate it.
7. Hold Trigger 2nd Stage AFTER the time/distance line flashes, but BEFORE the wings cue appears.
8. Follow the steering cue circle while continuing to hold trigger.
9. Bombs will fall automatically.

Dive Bomb (low precision)

Same procedure as above, but QFE is mandatory, stay in NAV mode, half-pull to show symbology, the bombs will drop immediately upon pulling the trigger to roughly where the pipper shows.

Radar Bomb

1. Set Radar mode A1, Find the target on the radar.
2. Weapon selector Bomb RR
3. Sight Mode Selector – Desired interval.
4. Set QFE on altimeter (required)
5. Master mode ANF
6. When approaching target, set radar range scale to 15km. You will see an additional cross at 3km. When the targets pass this line, Pull and hold trigger 2nd stage
7. Keep trigger held until all bombs are released (FALLD LAST)

NAV bomb

1. This method relies entirely on the nav system, ensure that your navigation point is accurate, that your nav system is accurate, and don’t expect precision results.
2. Approach target waypoint. Stay in NAV master mode.
3. Trigger UNSAFE
4. 2 seconds before release, distance line flashes. Pull and hold trigger.
5. Continue holding until you see FÄLLD LAST

TOSS bomb

1. The computer can toss bombs in the Radar or Nav attack profiles.
2. Estimate pull-up distance according to the following estimates (these are “max distance to pull up”, you can pull up sooner)
3. When the distance indicator indicates less than maximum release range for the current airspeed, start pulling up with 4g
4. When the climb angle is about +5deg, set trigger UNSAFE (can be set earlier).
5. Continue pitching up.
6. Markers appear on the distance line.
7. Pull and hold trigger
8. At 12-15deg climb angle, the bombs release automatically.
9. When you see FÄLLD LAST , turn and egress. Trigger safe.

  - Mach 0.8 – 4.4km
  - Mach 0.85 – 4.6km
  - Mach 0.9 – 4.8km

Plan Bomb

(wip)