1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

601 - Notes, Quirks, and Trivia

- To change radar range without pressing MFD buttons, quickly run radar cursor up past the top border of the radar window, then back down through the top border. Will increment range up, and wrap from 160 nm back to 5 nm. Do same on bottom of screen to decrease range.
- By default, the plane calculates your BINGO state to waypoint 0 (starting point). To make the plane calculate your BINGO state to a different waypoint, go to the FPAS page (SUPT menu) and set the HOME waypoint to the desired waypoint number.
- The sides of the canopy bow are roughly +/-30 degrees off the nose, for quick visual reference.
- You can toggle between the HSI map and SA page by repeatedly pressing Dish Hat down.
- The IFEI (engine monitor panel) color is controlled by the MODE switch on the Internal Lighting panel (right side console). DAY = White, NITE or NVG = Green. The brightness knob doesn't do anything in DAY mode.
- On the center MFD, if it's displaying the graphical map, the brightness knob at the top of the MFD is always disabled, and the brightness of the text is controlled automatically (in response to ambient light levels). With the map showing, if you press the DAY/NGT rocker to NGT, you can use the SYM, GAIN, and CONT rockers to adjust the brightness of the symbols and map to some extent (SYM seems to start maxed). Or if you press the DAY/NGT rocker to DAY, you can use SYM and GAIN but not CONT. If you turn the map off, then the brightness of the symbols is controlled with SYM and the brightness knob at the top. Any time the display flashes AUTO with a number, it means whatever you're changing is being overridden by the automatic controls.
- CMS programs from some online academy
  1. reactive flares
  2. preemptive (run in) flares
  3. 5. chaff