503 - A/G – Non-Visual (RR) Bombing Modes

Mixed weapon loadouts
- Mixed loadouts are not valid, except the following: RB-24/-24J A2A missiles are allowed with any loadout, and AKAN 30 mm gunpods are allowed with RB-75 (Maverick) or RB-05A (MCLOS) missiles.
- Release interval of 10-30m will produce a coherent stick of bombs, above 30m will lead to some un-asploded gaps between the bombs.

M/71 bombs (low drag) -- 120 kg (265 lb) GP bombs, 4 per pylon

RR Mode

Radar Bomb

1. Set Radar mode A1, Find the target on the radar.
2. Weapon selector Bomb RR
3. Sight Mode Selector – Desired interval.
4. Set QFE on altimeter (required)
5. Master mode ANF. Pole track will show commanded altitude, as determined by Ground Crew settings. You must fly the commanded altitude for the release to be accurate (TODO test to confirm). If you fly below this altitude, the bombs will not drop because the crew chief has deemed it unsafe.
6. When approaching target, set radar range scale to 15km. You will see an additional cross at 3km. When the targets pass this line, Pull and hold trigger..
  - If you have a target fix on the spot, you may get better results if you pull the trigger when the distance indicator shows 3km
Keep trigger held until all bombs are released (FALLD LAST)

NAV bomb

1. This method relies entirely on the nav system, ensure that your navigation point is accurate, that your nav system is accurate, and don’t expect precision results.
2. Approach target waypoint. Stay in NAV master mode.
3. Trigger UNSAFE. Pole track will show commanded altitude, as determined by Ground Crew settings. You must fly the commanded altitude for the release to be accurate. (TODO test to confirm). If you fly below this altitude, the bombs will not drop because the crew chief has deemed it unsafe.
4. 2 seconds before release, distance line flashes. Pull and hold trigger.
5. Continue holding until you see FÄLLD LAST

TOSS bomb

1. The computer can toss bombs in the Radar or Nav attack profiles. (it's awkward in radar though)
2. Estimate pull-up distance according to the following estimates (these are “max distance to pull up”, you can pull up sooner)
3. Set trigger UNSAFE
4. When the distance indicator indicates less than maximum release range for the current airspeed, start pulling up with 4g, and Pull and hold trigger.
5. Continue pitching up.
6. Markers appear on the distance line.
7. At 12-15deg climb angle, the bombs release automatically.
8. When you see FÄLLD LAST , turn and egress. Trigger safe.

  - Mach 0.8 – 4.4km
  - Mach 0.85 – 4.6km
  - Mach 0.9 – 4.8km