1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Landing, Navigation, Autopilot

Takeoff
1. Flaps half??
2. Rotate around 140 kts??
3. Hold 10 deg nose up and let the plane fly up off the runway. Don't exceed 13 degrees pitch or risk tailstrike.
4. Flaps up before 185 kts??
5. Gear up before 250 kts.

Navigation
- Press Bottom Hat Push to cycle NAV/LANDING to NAV mode.
  - NAV mode has radar altitude scale on right of HUD.
  - LANDING mode has VSI with pointer (VSI scale is shown at top; if blank, the top and bottom are 1000 ft/min, then 5 = 5000 ft/min, 10 = 10000 ft/min).
- Press Bottom Hat Fwd/Bk to change waypoints.
- HUD navigation info:
  - Navigation info is shown in bottom right of HUD:
    400R	Radar altitude
    2/32.7	Waypoint number (doesn't always seem to work??) / Distance to waypoint in nmi
    :06:25/-59.5	ETE in HH:MM:SS / TOT deviation in MM:SS, if + you're too slow, - you're too fast
    19:02:01	Current time
  - NOTE: Waypoint number is offset by one (e.g. waypoint 1 in mission editor shows as 2 in HUD).
  - Bearing to waypoint is "| |" indicator below heading tape at the bottom.
- HSI navigation info:
  - Needle on outside of compass dial shows bearing to selected waypoint.
  - Needle on inside of compass dial is Course Deviation Indicator; arrow points to heading to get back on course, center bar shows deviation from course.
  - Distance to waypoint is shown in top right corner.
- Bugs:
  - In LANDING mode, the airport ID never changes, always seems to show "2".
  - In NAV mode, the waypoint number shown in the HUD is one higher than your actual waypoint number.

Autopilot
Press MANVR/PC Push to turn on EAC (Enhanced Attitude Control system). EAC must be on in order for the autopilot to work.
  - There is no indicator in the cockpit showing EAC on or off.
1. Press MANVR/PC Down to toggle autopilot on/off.
2. Set autopilot mode with MANVR/PC Up for Path Hold (attitude hold) or MANVR/PC right for Altitude/Heading Hold (default).
  - After mode is changed, autopilot must be turned off and then back on to use that mode.
1. All autopilot modes, WIP:
  1. Altitude/Bank Hold
  2. Altitude/Heading Hold
  3. Path Hold (attitude hold)

Landing -- WIP but should be basically accurate
1. Speed brakes full out.
2. Gear down below 250 kts.
3. Flaps full down below 185 kts.
4. 500 fpm descent rate, onspeed AOA is shown with indicator on left side of HUD glass (around 120 kts when lightly loaded).
5. No need to flare??
6. NOTE: Wheelbrakes do not have antiskid. Brake carefully.
7. After stopping, retract airbrake, set flaps to half, and press Trim Reset button (Trim Hat Press).

ILS Landing
Press Bottom Hat Push to cycle NAV/LANDING to LANDING mode.
  - NAV mode has radar altitude scale on right of HUD.
  - LANDING mode has VSI with pointer (VSI scale is shown at top; if blank, the top and bottom are 1000 ft/min, then 5 = 5000 ft/min, 10 = 10000 ft/min).
Press Bottom Hat Fwd/Bk to change selected airport.
  - Airport ID is not shown anywhere in the A-10A, so you will have to guess based on distance and bearing.
1. HUD shows waypoint box at center of runway?? However distance is shown to runway threshold.
2. Artificial Horizon instrument will show ILS needles when closer than about 5 miles.