1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

101 - Controls - Joystick
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Trigger
P1: Trigger stage 1 (fires Laser designator or marker in TPOD/TRIG)	P2: Fire gun (gun only)
Flip-down Trigger -- Master Arm
Up: Master Safe	Dn: Master Arm	Pull: Laser Arm
Red Button
P: Weapon release (everything except gun)	S-P (3x): Eject
Upper Gray Button -- "NWS A/R DISC & MSL STEP"	SHIFT: COMM
On ground:
P: Toggle NWS ("AR NWS" light shows in small vertical light stack to right of HUD)
Air refueling:
P: Disconnect air refueling boom
A/A Master Mode or A/G Maverick MFD:
- P: Step to next weapon station.
- L-P: Select next weapon type.
A/G Master Mode (not Maverick):
P: Cycle CCRP, CCIP, DTOS modes
Lower Gray Button -- RWR Offset	SHIFT: Comm 1
Trim Hat
- U/D/L/R: in axis mode Pitch/Roll Trim	P: reset trim L-P: Switch Mode
- U:	L:
- D:	R:
Dish Hat -- "TMS/Target Management Switch"
SOI on HUD:
F: DTOS or Maverick visual designate	B: Target reject
SOI on MFD with radar in CRM mode (BVR):
- F: "Bug" or Lock target under cursor; in TWS also makes bugged target a System Target (hollow box)
- B: Target reject (un-bugs or unlocks target; in TWS un-sets System Targets)
- L/L-L: IFF Interrogate all targets/selected target
- R: Cycle TWS bug through System Targets (hollow boxes); if no TWS targets are System Targets, makes all TWS targets into System Targets
- L-R: Toggle TWS/RWS submode
SOI on MFD with radar in ACM mode:
- F: Boresight scan (or HMCS)
- B: If no target locked, Vertical scan; if target locked, Target Reject and radar off (NO RAD)
- R: HUD scan
- L: Slew scan??
SOI on MFD with TGP (TPOD):
- F: Point track
- L: Polarity swap
- R: Area track
SOI on MFD with Maverick:
- F: Lock target
- B: Target reject
- L: Polarity swap
SOI on MFD with HSD:
- F: Designate target
- B: Target reject
MANVR/PC hat -- "DMS/Display Management Switch"
- U: SOI to HUD
- D: SOI to MFD, swaps SOI to other MFD
- L-D: Toggles HMCS display
- L/R: Cycles left/right MFD page
Index Finger Hat -- View and Game controls
- F: VR Telescope	S-F: Rearm
- B: VR Zoom	S-B: Active Pause
- U: Mouse Click	S-U:
- D: Mouse Right Click	S-D: Show Controls
- P: VR Reset	S-P: Info Bar View Toggle
Gray Reset Hat -- Countermeasures & Autopilot
- F: Selected Program (bypass 1xeach)	S-F: Autopilot Pitch switch up
- B: Consent in SEMI, enables AUTO, ECM On	S-B: Autopilot Pitch switch down
- R: Disable Dispense, ECM Off	S-R: Autopilot Roll switch up
- L: CMS Left (does nothing??)	S-L: Autopilot Roll switch down
- P: Panic Countermeaures	S-P: Autopilot Pitch Switch OFF
Brake lever -- "Paddle switch"
P: Overrides autopilot while pressed