1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

103 - Controls - Throttle Base
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Red Start Button -- Master Caution Reset Audio Warning
Mode selector -- Countermeasure Mode
Detent Button -- Flashlight
Flaps lever – Flaps
TGL Switch – Gear	Shift: Hook
EN1 dial – Kneeboard & Selective Jettison
- P: Open Kneeboard	S-P: Jettison
- L/R: Page Left/Right	S-L/R: cw/ccw
E2 dial – NVGs & Volume
- P: Toggle NVGs on/off	S-P: Something RWR related
- L/R: NVG gain up/down	S-L/R: RWR Volume (or something)

Switch 1 -- Targeting System Power	SHIFT – HTS system power
Middle:
Switch 2 -- A/A Refueling Probe	SHIFT – CAT I (light A/A loadout)/CAT III (Heavy loadout)
Middle:
A1 –
A2 –
C1 Red Button – Emergency Jettison
B1 – MAIN PWR BATT	SHIFT – MAIN PWR/FWD
B2 – ENGINE FEED NORM	SHIFT – AIR SOURCE NORM
B3 – JFS START2	SHIFT – Startup Button 6
B4 – Startup Button 7	SHIFT – Startup Button 8
B5 – Canopy Down	SHIFT: Canopy Up