1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

101 - Controls - Joystick
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Trigger
- P1: --
- P2: Fire gun or A/A missile only; or laser designator or marker in TPOD/TRIG
Flip-down Trigger
Up: Master Safe	Dn: Master Arm	Pull: Laser Arm
Red Button
P: Weapon release (everything except gun and A/A missile)	S-P (3x): Eject
Upper Gray Button Undesignate / NWS On-Hi	Shift Comm
Lower Gray Button RWR Offset	Shift Comm 1
Trim Hat (long press to switch between axis and hat modes)
- U/D/L/R: in axis mode Pitch/Roll Trim
- U: SA Scale	L: SA Map
- D: SA Step	R: SA DCNTR
MANVR/PC hat -- "SCS/Sensor Control Switch"
A/A Master Mode, Radar in any BVR mode (RWS/TWS/STT/etc.):
- U: Radar to ACM mode, Boresight/HACQ scan, 10 nmi range
- L-U: Radar to ACM mode, Boresight/LACQ scan, 40 nmi range
- D: SOI to center MFD, swap HSI and SA page.
- L: SOI to left MFD, set left MFD to AZ/EL page, toggle AZ/EL and FLIR PNT page
- R: SOI to right MFD, set right MFD to AZ/EL page, toggle AZ/EL and FLIR PNT page
  If MFD already has SOI, automatically locks up either the target currently under the cursor, or the closest target, or unlocks if target is locked.
A/A Master Mode, Radar in ACM mode:
- U: Boresight/HACQ scan, 10 nmi range
- L-U: Boresight/LACQ scan, 40 nmi range
- D: VACQ (vertical) scan, 5 nmi range
- L: WACQ (wide) scan, 10 nmi range, 60 deg azimuth, +6/-9 deg elevation, slaved to aircraft in pitch, horizon in roll
- R: --
A/G Master Mode:
- U: SOI to HUD/HMD
- D: SOI to center MFD
- L: SOI to left MFD
- R: SOI to right MFD
  If FLIR MFD already has SOI, hat toward FLIR toggles through tracking modes: none, ATRK, PTRK.
  In A2G radar GMT or SEA mode, hat toward radar MFD locks target under TDC cursor.
Dish hat – Weapon Select (long press pov mode unbound)
- F: Selects AIM-7, radar 4-bar scan, 140 degrees, 40 miles
- B: Selects gun, radar 5-bar GACQ vertical scan, 5 miles
- R: Selects AIM-120, radar 4-bar scan, 140 degrees, 80 miles for AIM-120B, 160 miles for AIM-120C
- L: Selects AIM-9, radar 4-bar scan, 90 degrees, 10 miles for AIM-9P/M, 20 miles for AIM-9X
Index Finger Hat -- View and Game controls
- F: VR Telescope	S-F: Rearm
- B: VR Zoom	S-B: Active Pause
- U: Mouse Click	S-U:
- D: Mouse Right Click	S-D: Show Controls
- P: VR Reset	S-P: Info Bar Toggle
Thumb Reset Hat – "Countermeasure Switch"
Pressing any of these automatically sets you to A/A Master Mode.
- F: CMS Aft, Flare (bypass) or selected program 5
- B: CMS Forward, Chaff (bypass) or program 5
- R: ECM Xmit
- L: ECM RCV
- P: Panic Countermeaures (program 6, 40 chaff 40 flare by default)
Brake lever -- "Paddle switch"
P: NWS disengage, AP disengage, G-limiter override
Grip Button – SHIFT