506 - A/G - RB 05 MCLOS missile

Before attack:
1. Set Weapon Selector dial depending on attack profile:
  1. MARK DYK for ground targets, detonates on impact.
  2. SJO PLAN for naval targets, detonates after short delay.
  3. LUFT RR for air targets, detonates when within 6 m of target.
2. Missile range approx 10 km, battery life is 40 seconds from Trigger Unsafe.

On attack run toward target waypoint:
1. Set Master Mode dial to ANF.
2. When 10 away, set Trigger Unsafe (hold Trigger 1st stage, or press Flip-down trigger).
  - IMPORTANT: Missile battery lasts only 40 seconds starting when Trigger Unsafe is pressed.
1. Press Trigger 2nd stage to fire.
2. Guide missile visually with RB 05 stick pitch up/down/left/right (Dish Hat up/down/left/right, or Pull Lever to make main flight stick steer the missile)

Tips:
- Get some altitude for the attack run, over 1km for good results
- Use attitude hold on the dive and use the pull lever for best control (should this be moved to a different control on the left hand? When I tried yesterday I was getting some weird pitch and roll behavior on the plane, maybe because squeezing the lever puts some force on the stick)