202 - Ground - Preflight, Limits

Preflight -- Strikeout indicates step not needed after Havoc's Quick Autostart script
1. Backup ADI power switch ... ON (middle position) (right console middle, far outboard)
2. Set up navigation:
  1. Set up waypoint markers on map, see other page for marker types.
  2. Open kneeboard and go to page showing data cartridge source. LCtrl-LAlt-C to increment source, LCtrl-LShift-C to decrement. (S-Switch 2 Up/Dn)
  3. Insert (or remove and re-insert) data cartridge (behind left elbow).
  4. Data selector knob ... REF LOLA, IN, enter 9099, press LS/SKU, wait for display to show zeros
  5. Data selector knob ... AKT POS, OUT
  6. Do a sanity check on the waypoints. Make sure you have a target (Mn) waypoint. If not, use TAKT, IN, 9, <waypoint button> to change Bn into Mn, or 0, <waypoint button> for Mn into Bn.
3. Set up weapons:
  1. Altimeter QFE ... As needed to match value shown in kneeboard for target waypoint
  2. Weapon Selector dial ... As needed (see A/G weapons pages) (right wall)
  3. Interval dial ... As needed (see A/G weapons pages) (right wall)
4. HUD glass position ... As needed (Upper Grey Button)
5. SLAV SI switch ... F (turns off HUD declutter at low altitude) (right instrument panel top)
6. Master Mode knob ... NAV
7. Radios ... As needed (left console forward), see other page for more info, or use manual tuning:
  1. Press "‒" button, set frequency with dials on bottom left instrument panel.
8. Countermeasures ... As needed, see other page for more info, must have 1 or 2 CM pods for chaff/flares and/or 1 ECM pod for jamming, recommended settings:
  1. CM Mode knob ... 1 for rapid release (0.85 sec), 2 for medium (2.0 sec), 3 for slow (4.5 sec)
  2. CM Type knob ... RF (allows both chaff and flares)
  3. CM Streak knob ... 0 (dispense from pods at the same time)
  4. For U22 ECM pod:
    1. Jammer Mode knob ... B for warmup (3 mins, KB-H/KA SL lit), then A for jamming
    2. Jammer Band knob ... doesn't matter
  5. For U22/A ECM+ELINT pod:
    1. Jammer Mode knob ... A for warmup (3 mins, KB-H/KA SL lit), then A for ELINT or B for ECM
    2. Jammer Band knob ... K for sensitivity auto cycle
  - Press Countermeasures Quick Release button on throttle (CMS Fwd) to toggle continuous dispensing of chaff and flares, 1x of each every 2.0 seconds.
  - Or set Countermeasures Dispensing switch (left canopy rail) to KONT (CMS Back to toggle through positions) to toggle continuous dispensing of chaff only according to CM Mode knob.
  - Pods have 72 flares and 212 chaff each. Changing these quantities breaks the dispense interval settings (openbeta 2.7.11.21408.1 patch notes).
Lights ... As desired:
  - Instrument, warning panel, cockpit flood lights, and radar screen ... left console rear inboard knobs
  - Anticollision, navigation, formation, and position lights ... right console rear inboard switches
  - HUD brightness ... knob to left of HUD/gunsight base
  - Taxi/landing lights ... hidden under left forward canopy rail next to thrust reverser
RWR volume ... As desired (shift-E2 rotate, or LJUDSTYRKA knob on left wall panel)
Mixed A/G armament is generally not allowed. Only exceptions are gun pods + RB 75 Mavericks or gun pods + RB 05A missile. Sidewinders can be carried with any A/G stores though.

Performance limits:
- Fuel: 9,868 lbs internal (103% on gauge)
  - with drop tank (2,233 lbs) = 12,101 lbs (125% on gauge)
- Landing gear: 600 kph
- Best fuel economy: 0.55 Mach at 0 m, +0.11 Mach per 3,000 m/10,000 ft
- Max AB altitude: approx 14,500 m
- Airbrakes max speed: Mach 0.92