505 - A/G - RB 04E antiship missiles (older missiles)

Ground Setup
RB-04 missiles need to be pre-programmed by the ground crew if they are to differ from their default behavior. There are two main modes, Single, for single radar contacts or Group for grouped contacts (assumed to be transports or landing craft).

Due to the behavior of the seeker, it is strongly recommended to plan attacks in wide formation, preferably from multiple angles to prevent multiple missiles hitting the same ship.

Alter the missile's behavior while on the ground via the kneeboard page "Groundcrew Settings". See below.

Before any attack
1. Weapon Selector dial to ATTACK, Release Mode switch as needed. If SERIE is used, missiles will automatically separate after launch.
2. Set QFE on altimeter to QNE (sea level pressure).
3. Height 50 m to 425 m.
4. Range 24 km (13.0 nmi) max, 12 km (6.5 nmi) min
5. Missile's radar range 8 km (4.3 nmi), FOV +/-28 deg.

Quick attack in NAV mode using default missile behavior
1. Set Master Mode dial to NAV.
2. Targeting Mode switch to ENKEL (single target) or GRUPP (targets in group within 2.7 km and in line parallel to missile travel)
1. Point plane at ships (either visually or using radar).
2. (Optional) Set target waypoint at ships, set Master Mode dial to ANF. Ranging cues will appear on radar screen.
3. Press and hold trigger until missile fires. Missiles will immedately drop to 10 m ASL and fly in a straight line until they find targets with their radar, and attack the first one (or group) they see.

Planned attack
- Group Target: If MALVAL Targeting Mode switch is set to GRUPP missile will select three or more contacts that form a "group". To be a "group", the contacts must be within 2700 meters of each other in depth along the axis of the missile's travel. If the missile is told to target a group but cannot find one, it will ignore those contacts and continue flying.
  - This is important: three ships in a bow-to-stern row attacked from the side is not a group, a missile shot in group mode won't attack these. If attacking from the side, the ships need to be line abreast for the missile to consider them a group. Similarly, if attacking from the bow, three ships traveling abreast are not a group, three ships in a row bow-to-stern are.
  - The contacts also need to be spotted in the same range sweep for the missile to recognize them.
- The "group target" setting in the ground crew kneeboard determines how many rows of ships the missile will skip inside the group before it attacks. 1 means it attacks the first ship. 2 means it flies over the first ship and attacks the second. Etc.
- The "angle jump" setting directs the missile to skip the first target or group it could possibly attack and select the next one, provided it identifies it before reaching the end of the radar sweep and coming back around. This is useful to make one of two missiles launched at the same time attack different targets/groups.